Processing of the line AVO 12.

This is a public domain line from the Mobil Viking Graben dataset.
The line is available as a SEG Y file at 4 ms sample interval. There is also a far-field signature but at 1 ms sample interval.

Acquisition parameters
120 channels
receiver interval 25 m
shot interval 25 m
near offset	262 m
cable depth	10 m
gun depth	6 m

The data quality is good with no dead channels. There are misfires when 2 or 3 consecutive shots were missed. The water bottom depth varies little.

The SEG Y data file was read. The trace headers contained CDP numbers and coordinates, so geometry definition was not necessary.

Shot amplitude normalisation was the only preliminary processing step.

The data was sorted to common offset gathers. Noise attenuation was effected by f-x decon.
This used an operator of 5 points in a window 21 traces by 600 ms.

Phase-only designature was done using the far-field signature.

Missing trace interpolation was performed on these gathers to restore missing shots.

The data was sorted to CDP gathers and a semblance velocity analysis was created at interval of 120 CDPs. First pass velocities were picked. These were used to create a brute stack.

The data was also sorted back to shot gathers. Near traces were extrapolated for surface multiple attenuation (SMA) using first-pass velocities. A head mute was applied to remove direct wave and refractions. The SMA multiple estimate was computed over range of 5 to 60 Hz, then the multiples removed by adaptive subtraction, starting at 900 ms with window of 200 ms.

The SMA shots were sorted to CDP gathers and another semblance velocity analysis done at interval of 120 CDPs.

Radon demultiple was performed with second-pass velocities. This was parabolic radon over
6 to 80 Hz rejecting multiples with moveout 0.06 to 0.8 seconds at far offset.

Finally, residual moveout trim was computed for a range of 12 ms at far offset and applied to the gathers, and final stack output.