Processing of Alaska 2D line 31-81 and 16-81

Background
This is a public-domain line, which has been processed by SU, so it has been processed with CPSeis for comparison. It is a small dataset, and processing runtime is short. It was commercially processed in 1981, which provides a guide for this project. It is available from USGS website. It can be found via
http://wiki.seg.org/index.php/Open_data

Acquisition parameters
96 channel split spread with 110 foot spacing
Source interval 440 foot, centre between channels 48 and 49
Shothole depth 75 foot
Record length 6 seconds at 2 ms sampling

Data Quality
The raw shots show reflectors. The far offset is only 5225 feet, so normal moveout is not much for demultiple techniques. There is some impact noise, probably from holes blowing out. The near traces are quite noisy, as they were only 55 feet from the hole. Elevation changes are modest, and statics do not appear significant.

Processing flow line 31

Three SEG Y files were read and concatenated. Trace edits were applied. Gain recovery was applied with time to the power 2. Geometry was setup in CFG program and applied to the trace headers.

To remove some of the impact noise, median despike was used. The traces were first sorted into common channel gathers. The median despike used a window of 5 traces by 120 ms, and the threshold was 4.

Surface wave were attenuated by an f-k filter. The traces were sorted back into shot gathers. Before the f-k filter, removable AGC was applied with window length 500 ms. Also normal moveout was applied using an average stacking velocity from previous processing. The f-k filter was designed to pass dips less than 4 ms per trace, and reject dips greater than 12 ms per trace.
The normal moveout and AGC were removed after filtering.

The traces were then sorted to CDP gathers, and semblance velocity analysis run. The analysis interval was 50 CDPs or 2750 feet. Velocities were picked with VA program. Following this, an initial stack can be created. An inner trace mute was used below 1.4 seconds, as the near traces were noisy.

Next surface-consistent residual statics were run. CPSeis has three modules for this, and little difference resulted, whichever was used. Three iterations were run with a maximum shift of 6 ms

After residual statics, further velocity analysis was done by creating constant-velocity stacks for the full-fold portion of the line. This was to refine the picking of shallower events above 1 second.

After obtaining a final stacking velocity, residual moveout was applied using the VTRIM module. A maximum moveout of 8 ms was allowed between 1 and 4 seconds.

A stack was created from the residual moveout gathers. Predictive deconvolution was applied after stack, using a gap of 40 ms and operator of 200 ms. Finally f-x decon was used to attenuate some of the remaining noise. This used an operator of 5 points in a window of 21 traces by 600 ms.

Processing flow line 16-81

Having established the processing sequence, it was followed for line 16-81, with the following changes:

Median despike used window of 7 traces by 100 ms.

f-k filter reject dips greater than 16 ms/trace

Velocity analysis at interval of 48 CDPs or 2640 feet.

Residual statics maximum shift of 8 ms.